MASTER PATIENT INDEX

(MPI) VISTA

HL7 INTERFACE SPECIFICATIONS

Version 1.0

April 1999

# Department of Veterans Affairs

VISTA Technical Services

Standard Files and Indexes

Contents

Figures	v

Introduction	1

Assumptions	1

Message Content	1

Data Capture and Transmission	1

Background Messages	1

Batch Messages	2

Batch Acknowledgments	2

Direct Connect	2

HL7 Control Segments	5

Message Definitions	5

Segment Table Definitions	5

Message Control Segments	5

MSH	— Message Header Segment	7

BHS	— Batch Header Segment	9

BTS	— Batch Trailer Segment	10

NTE	— Notes and Comments Segment  (Change CMOR A31)	10

NTE	— Notes and Comments Segment  (Batch CMOR Comparison)	10

MSA	— Message Acknowledgment Segment	11

EVN	— Event Type Segment	11

PID	— Patient Identification Segment	11

PD1	— Patient Demographic	13

ZPD	— VA specific Patient Information Segment	13

PV1	— Patient Visit Segment	14

MRG	— Merge Patient Information	16

MFI	— Master File Identification Segment	16

MFE	— Master File Entry Segment	17

VTQ	—  Attributes	17

RDF	— Table Row Definition Segment	18

RDT	— Table Row Data Segment	18

ZEL	— VA specific Patient Eligibility Segment	19

ZSP	— VA specific Service Period Segment	19

ZCT	— VA Specific Emergency Contact Segment	20

ZEM	— VA Specific Employment Information Segment	20

ZFF	— VA Specific File/Field Segment	21

OBX	— Observation/Result Segment	21

Unsolicited HL7 Messages	23

Trigger Events and Message Definitions Broadcast to Sites and to the MPI	23

ADT A04 Message — Register a Patient	23

ADT A08 Message — Update Patient Information	24

ADT A28 Message — Adding a New Patient	27

ADT A29 Message — Delete Person Information	28

ADT A30 Message — Merge Person Information	28

MFN — Update Treating Facility	29

VQQ — Virtual Table Query (Event Q01)	30

Trigger Events and Message Definitions Received	33

VQQ — Virtual Table Query Response	33

ADT A31 Message — Update Person Information	34

ADT A31 Message — Change CIRN Master of Record (CMOR)	35

ADT A31 Message — Batch CMOR Comparison	36

Appendix A	39

HL7 Standard Tables	39

VA Specific Tables	45

Figures

Figure 1: HL7 Message Header Segment (MSH)	8

Figure 2: HL7 Batch Header Segment (BHS)	10

Figure 3: HL7 Batch Trailer Segment (BTS)	10

Figure 4: HL7 Notes and Comments Segment (NTE) — Change CMOR A31	10

Figure 5: HL7 Notes and Comments Segment (NTE) — Batch CMOR Comparison	10

Figure 6: HL7 Message Acknowledgment Segment (MSA)	11

Figure 7: HL7 Event Type Segment (EVN)	11

Figure 8: HL7 Patient Identification Segment (PID)	12

Figure 9: HL7 Patient Demographic (PD1)	13

Figure 10: HL7 VA specific Patient Information Segment (ZPD)	14

Figure 11: HL7 Patient Visit Segment (PV1)	15

Figure 12: HL7 Merge Patient Information (MRG)	16

Figure 13: HL7 Master File Identification Segment (MFI)	16

Figure 14: HL7 Master File Entry Segment (MFE)	17

Figure 15: HL7 Attributes (VTQ)	17

Figure 16: HL7 Table Row Definition Segment (RDF)	18

Figure 17: HL7 Table Row Data Segment (RDT)	18

Figure 18: HL7 VA specific Patient Eligibility Segment (ZEL)	19

Figure 19: HL7 VA specific Service Period Segment (ZSP)	19

Figure 20: HL7 VA Specific Emergency Contact Segment (ZCT)	20

Figure 21: HL7 VA Specific Employment Information Segment (ZEM)	20

Figure 22: HL7 VA Specific File/Field Segment (ZFF)	21

Figure 23: HL7 Observation/Result Segment (OBX)	21

Figure 24: HL7 ADT A04 message type (Register a Patient)	23

Figure 25: Sample HL7 ADT A04 message (Register a Patient)	24

Figure 26: Data elements monitored in the PATIENT file (file #2) for changes	25

Figure 27: HL7 ADT A08 message type (Update Patient Information)	26

Figure 28: Sample HL7 ADT A08 message (Update Patient Information)	26

Figure 29: HL7 ADT A28 message type (Adding a New Patient)	27

Figure 30: Sample HL7 ADT A28 message (Adding a New Patient)	27

Figure 31: HL7 ADT A29 message type (Delete Person Information)	28

Figure 32: Sample HL7 ADT A29 message (Delete Person Information)	28

Figure 33: HL7 ADT A30 message type (Merge Person Information)	29

Figure 34: Sample HL7 ADT A30 message (Merge Person Information)	29

Figure 35: HL7 Update Treating Facility message type (MFN)	29

Figure 36: Sample HL7 Update Treating Facility (MFN) message from Owner	30

Figure 37: Sample HL7 Update Treating Facility (MFN) message from Non–owner	30

Figure 38: HL7 Virtual Table Query (VQQ) message type — Event Q01	30

Figure 39: Sample HL7 Virtual Table Query (VQQ) message — Event Q01 (MPI Batch Initialization)	31

Figure 40: Sample HL7 Virtual Table Query (VQQ) message — Event Q01 (Direct Connect Query)	32

Figure 41: HL7 Virtual Table Query Response (VQQ) message type	33

Figure 42: Sample HL7 Virtual Table Query Response (VQQ) message — MPI Batch Initialization	34

Figure 43: HL7 ADT A31 message type (Update Person Information)	35

Figure 44: Sample HL7 ADT A31 message (Update Person Information)	35

Figure 45: HL7 ADT A31 message type [Change CIRN Master of Record (CMOR)]	35

Figure 46: Sample HL7 ADT A31 Message [Change CIRN Master Of Record (CMOR)]	36

Figure 47: HL7 ADT A31 message type (Batch CMOR Comparison)	36

Figure 48: Sample HL7 ADT A31 message (Batch CMOR Comparison)	37

Introduction

This interface specification is intended to identify the VISTA information that will be shared as part of the CIRN/Master Patient Index (MPI) project. The sharing of this information will be triggered by specific VISTA events. Both the exact events and the messages used to share this data will be reviewed.

The MPI application will make use of and create messages using the abstract message approach and encoding rules specified by the HL7 standard. The HL7 VISTA application will be used for communicating data associated with various events that occur in health care environments.

The formats of these messages conform to the HL7 interface standards, Version 2.3. HL7 custom message formats (“Z” segments) are used only when necessary.

## Assumptions

This interface document assumes that communication between the systems is established and maintained by VISTA/Kernel processes. The discussion of specific technical issues related to this aspect of communication is beyond the scope of this document. This document also assumes a communication server utilizing VISTA HL7 version 1.6 or a similar compatible message communicator. VISTA Kernel, MailMan, VA FileMan, and HL7 package are assumed the most recent versions and fully patched.

## Message Content

The data sent in the HL7 messages will only be limited by the data available in VISTA. The messages used will be generic enough so that any application or external system should be able to find all the information that is relative to the event that triggered it.

Several different HL7 messages are available. MPI VISTA takes advantage of VISTA events and has added some new events to support the MPI.

## Data Capture and Transmission

When a PIMS, CIRN, or MPI option, call, or API is used to update a specific patient's information in VISTA, an HL7 message is triggered to broadcast the event. Any changes made to patient information in nonstandard ways, such as direct global sets by an application or by MUMPS (M) code will not trigger a broadcast message.

## Background Messages

Updates to specific patient demographic data will trigger the broadcasting of a HL7 ADT-A08 message. Because there is no set way of identifying when an edit to patient information is complete, these edit events are marked as needing to be transmitted in the ADT/HL7 Pivot file. A background job (scheduled TaskMan job) periodically broadcasts the HL7 ADT-A08 message, containing any changes to data.

Updates to a patient’s treating facility list function in a similar manner. When the update to a patient’s treating facility occurs this event is added to the ADT/HL7 Pivot file and marked for transmission. A background job will collect these updates and broadcast the HL7 MFN messages.

Background processes are also used during the initialization phase of the MPI. Specifically a background process creates batch messages of patients requesting assignment of ICNs by the MPI. These patients have been assigned a CMOR Activity Score during the Pre-Implementation phase of CIRN/MPI.

Following the initialization process, a batch CMOR comparison background job is started. This job sends HL7 batch messages comprised of non-CMOR (requesting site) patient entries (100 maximum per HL7 batch message) to determine, based upon CMOR Activity Score, if the CMOR should be changed to the requesting site. If it is determined that a patient's CMOR needs to be changed, a single HL7 message is generated for this purpose. The HL7 message is sent from the CMOR to all sites where that patient has been seen and to the MPI.

The Local and Missing ICN background process looks at the Local ICN and Missing ICN cross-reference and sends batch messages to the MPI requesting an ICN. Patients can receive a Local ICN if an attempt to contact the MPI fails. The Missing ICN cross-reference is set if a package outside of PIMS adds a patient to the Patient file.

## Batch Messages

Batch messages will be used to send queries to the MPI for ICN during the initialization process, and for resolution of Local or Missing ICNs.

The CMOR Comparison background job sends batch messages to the current CMOR from a non-CMOR requesting the CMOR be changed. This is a process that happens after the MPI Initialization and makes the determination to change the CMOR based upon the CMOR Activity Score, with no user intervention.

## Batch Acknowledgments

The acknowledgments returned during the initialization process and the Local/Missing ICN Resolution job are processed through a background job that files the ICN, ICN checksum, and CMOR and updates the Treating Facility list. The return of this data constitutes the acknowledgment of the batch message.

## Direct Connect

The Direct Connect is a real-time TCP/IP connection to the Master Patient Index to allow for an immediate request for an ICN. It is activated during the Register A Patient, Load/Edit Patient Data, and 10-10T Registration processes when:

1)	a new patient is added to the system, or

2)	when a patient exists but doesn't have an ICN

In addition, by utilizing the new option Single Patient Initialization to MPI, the TCP/IP direct connection with the MPI will occur. This event causes creation of a VTQ-Q02 and is sent to the MPI to find out if the patient is known. If the MPI returns a message stating that the patient is not known, an ADT-A28 Add Person message is then sent to the MPI. If the patient was known or added via the ADT-A28 message, the MPI will return the known information and the patient's entry is updated.

The new Display Only Query option to view the data the MPI knows about a patient also utilizes the TCP/IP direct connect with the MPI. A VTQ query is sent to the MPI. If the MPI knows the patient or finds a list of potential matches, the data is displayed to the users. No data is updated at the site or the MPI. If the MPI does not know the patient, a message is displayed stating so.

Documentation on the setup and use of this TCP/IP link is provided by the KERNEL patch # XU*8.0*54. Readers are also advised to familiarize themselves with the HL7 manual, V 1.6 and the following related patches:

HL*1.6*43

HL*1.6*19

HL*1.6*39

# HL7 Control Segments

This section defines the HL7 control segments supported by VISTA. The messages are presented separately and defined by category; segments are also described. The messages are presented in the following categories:

- Message Control

- Unsolicited Transactions from VISTA

## Message Definitions

From the VISTA perspective, incoming or outgoing messages are handled or generated based on an event.

In this section, and the sections following, these elements will be defined for each message:

- The trigger events

- The message event code

- A list of segments used in the message

- A list of fields for each segment in the message

Each message is composed of segments. Segments contain logical groupings of data. Segments may be optional or repeatable. A [ ] indicates the segment is optional, the { } indicates the segment is repeatable. For each message category there will be a list of HL7 standard segments and/or "Z" segments used for the message.

## Segment Table Definitions

For each segment, the data elements are described in table format. The table includes the sequence number (SEQ), maximum length (LEN), data type (DT), required or optional (R/O), repeatable (RP/#), the table number (TBL #), the element name, and the VISTA description. Each segment is described in the following sections.

## Message Control Segments

This section describes the message control segments, which are contained in message-types described in this document. These are generic descriptions. All of the segments described in this section are included in messages in this document. The VISTA descriptions and mappings will be as specified here unless otherwise noted.

- MSH	—	Message Header

- BHS	—	Batch Header Segment

- BTS	—	Batch Trailer Segment

- NTE	—	Notes and Comments Segment  (Change CMOR A31)

- NTE	—	Notes and Comments Segment  (Batch CMOR Comparison)

- MSA	—	Message Acknowledgment Segment

- EVN	—	Event Type Segment

- PID	—	Patient Identification Segment

- PD1	—	Patient Demographic

- ZPD	—	VA specific Patient Information Segment

- PV1	—	Patient Visit Segment

- MRG	—	Merge Patient Information

- MFI	—	Master File Identification Segment

- MFE	—	Master File Entry Segment

- VTQ	—	Attributes

- RDF	—	Table Row Definition Segment

- RDT	—	Table Row Data Segment

- ZEL	—	VA specific Patient Eligibility Segment

- ZSP	—	VA specific Service Period Segment

- ZCT	—	VA Specific Emergency Contact Segment

- ZEM	—	VA Specific Employment Information Segment

- ZFF	—	VA Specific File/Field Segment

- OBX	—	Observation/Result Segment

| MSH — Message Header Segment |
| --- |
| SEQ | LEN | DT | R/O | RP/# | TBL# | Element Name | VISTA Element Name |
| 1 | 1 | ST | R |  |  | Field Separator | Recommended value is ^ (caret) |
| 2 | 4 | ST | R |  |  | Encoding Characters | Recommended delimiter values: Component = ~ (tilde) Repeat = ¦ (bar) Escape = \ (back slash) Subcomponent = & (ampersand) |
| 3 | 15 | ST |  |  |  | Sending Application | When originating from facility and the message type is ADT or a Treating Facility Update or an A28 Add Patient: VAFC PIMS When originating from facility and the message type is a query via the Direct Connect: MPI_LOAD When originating from MPI: MPI For batch queries: MPI-STARTUP Batch CMOR Comparison: CMOR COMPARISON Change CMOR: CMOR COM RESULT |
| 4 | 20 | ST |  |  |  | Sending Facility | When originating from facility: Station's facility number When originating from MPI: MPI |
| 5 | 30 | ST |  |  |  | Receiving Application | When originating from facility and the message type is ADT: RG CIRN Treating Facility Update: VAFC PIMS When originating from MPI (not during Initialization) or A28 Add Patient: MPI Direct Connect Query: MPI_ICN From MPI during Initialization: MPI_STARTUP For batch queries: MPI Change CMOR (A31): CMOR COM RESULT Update Patient Data (A31): MPI_LOAD |
| 6 | 30 | ST |  |  |  | Receiving Facility | When originating from facility: Station # When originating from MPI: 200M |
| 7 | 26 | TS |  |  |  | Date/Time Of Message | Date and time message was created |
| 8 | 40 | ST |  |  |  | Security | Not used |
| 9 | 7 | CM | R |  | 0076 0003 | Message Type | Component 1: Refer to table 0076 Component 2: Refer to table 0003 |
| 10 | 20 | ST | R |  |  | Message Control ID | Automatically generated by VISTA HL7 Package |
| 11 | 1 | ID | R |  | 0103 | Processing ID | P (production) |
| 12 | 8 | ID | R |  | 0104 | Version ID | 2.3 (version 2.3) |
| 13 | 15 | NM |  |  |  | Sequence Number | Not used |
| 14 | 180 | ST |  |  |  | Continuation Pointer | Not used |
| 15 | 2 | ID |  |  | 0155 | Accept acknowledgment Type | NE (never acknowledge) |
| 16 | 2 | ID |  |  | 0155 | Application acknowledgment Type | AL (always acknowledge) |
| 17 | 3 | ID |  |  |  | Country Code | USA |
| 18 | 6 | ID |  | Y/3 | 0211 | Character Set | ASCII |
| 19 | 60 | CE |  |  |  | Principal Language of Message | Not used |

Figure 1: HL7 Message Header Segment (MSH)

| BHS — Batch Header Segment |
| --- |
| SEQ | LEN | DT | R/O | RP/# | TBL# | Element Name | VISTA Element Name |
| 1 | 1 | ST | R |  |  | Batch Field Separator | Recommended value is ^ (caret) |
| 2 | 4 | ST | R |  |  | Batch Encoding Characters | Recommended delimiter values: Component = ~ (tilde) Repeat = ¦ (bar) Escape = \ (back slash) Subcomponent = & (ampersand) |
| 3 | 15 | ST |  |  |  | Batch Sending Application | When originating from facility and is MPI Initialization: MPI-STARTUP When originating from MPI in response to Initialization: MPI CMOR Batch Comparison: CMOR COMPARISON |
| 4 | 20 | ST |  |  |  | Batch Sending Facility | When originating from facility: Station's facility number When originating from MPI: 200M |
| 5 | 15 | ST |  |  |  | Batch Receiving Application | When originating from facility for Initialization: MPI CMOR Batch Comparison: CMOR COMPARISON When originating from MPI: MPI_STARTUP |
| 6 | 20 | ST |  |  |  | Batch Receiving Facility | When originating from facility: MPI When originating from MPI: Station's facility number |
| 7 | 26 | TS |  |  |  | Batch Creation Date/Time | Date and time batch message was created |
| 8 | 40 | ST |  |  |  | Batch Security | Not used |
| 9 | 20 | ST |  |  |  | Batch Name/ID/Type | Component 1: Not used Component 2: P Component 3: Sub Component 1: message type Sub Component 2: event type code Component 4: 2.3 |
| 10 | 80 | ST |  |  |  | Batch Comment | Component 1: Refer to table 0008 Component 2: Text Message |
| 11 | 20 | ST |  |  |  | Batch Control ID | Automatically generated by VISTA HL7 Package |
| 12 | 20 | ST |  |  |  | Reference Batch Control ID | Batch Control ID of batch message being acknowledged |

Figure 2: HL7 Batch Header Segment (BHS)

### BTS	—	Batch Trailer Segment

| SEQ | LEN | DT | R/O | RP/# | TBL# | Element Name | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 10 | ST |  |  | 0093 | Batch Message Count | Number of messages within batch |
| 2 | 80 | ST |  |  | 0094 | Batch Comment | Not used |
| 3 | 100 | CM |  | Y | 0095 | Batch Totals | Not used |

Figure 3: HL7 Batch Trailer Segment (BTS)

### NTE	—	Notes and Comments Segment  (Change CMOR A31)

| SEQ | LEN | DT | R/O | RP/# | TBL# | Element Name | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 4 | SI |  |  |  | Set ID | Not used |
| 2 | 8 | ID |  |  | 0105 | Source of Comment | P |
| 3 | 64k | FT |  | Y |  | Comment | Component 1: Phone Component 2:Reason for request Component 3: Status Component 4: ID (.01 field of request) Component 5: Requestor (Station Number of CMOR) |

Figure 4: HL7 Notes and Comments Segment (NTE) — Change CMOR A31

### NTE	—	Notes and Comments Segment  (Batch CMOR Comparison)

| SEQ | LEN | DT | R/O | RP/# | TBL# | Element Name | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 20 | ST |  |  |  | Reason | COMPARISON |
| 2 | 3 | ST |  |  |  | CMOR Station | Station # of CMOR |

Figure 5: HL7 Notes and Comments Segment (NTE) — Batch CMOR Comparison

| MSA — Message Acknowledgment Segment |
| --- |
| SEQ | LEN | DT | R/O | RP/# | TBL# | Element Name | VISTA Element Name |
| 1 | 2 | ID | R |  | 0008 | Acknowledgment Code | Refer to table 0008 |
| 2 | 20 | ST | R |  |  | Message Control ID | Message Control ID of message being acknowledged |
| 3 | 80 | ST |  |  | NPCD 001 | Text Message | Description of event |
| 4 | 15 | NM |  |  |  | Expected Sequence Number | Not used |
| 5 | 1 | ID |  |  | 0102 | Delayed Acknowledgment Type | Not used |
| 6 | 100 | CE |  |  |  | Error Condition | Description of error condition |

Figure 6: HL7 Message Acknowledgment Segment (MSA)

### EVN	—	Event Type Segment

| SEQ | LEN | DT | R/O | RP/# | TBL# | Element Name | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 3 | ID | R |  | 0003 | Event Type Code | Refer to table 0003 |
| 2 | 26 | TS | R |  |  | Recorded Date/Time | Date/Time event occurred |
| 3 | 26 | TS |  |  |  | Date/Time Planned Event | Not used |
| 4 | 3 | ID |  |  | 0062 | Event Reason Code | Refer to table 0062 |
| 5 | 60 | CN |  |  |  | Operator ID | User causing event |
| 6 | 26 | TS |  |  |  | Event Occurred | Not used |

Figure 7: HL7 Event Type Segment (EVN)

| PID — Patient Identification Segment |
| --- |
| SEQ | LEN | DT | R/O | RP/# | TBL# | Element Name | VISTA Element Name |
| 1 | 4 | SI |  |  |  | Set ID - Patient ID | Sequential Number |
| 2 | 20 | CK |  |  |  | Patient ID (External ID) | Integration Control Number (ICN) |
| 3 | 21 | CM | R | Y |  | Patient ID (Internal ID) | Pointer to entry in PATIENT file |
| 4 | 12 | ST |  |  |  | Alternate Patient ID | Primary Short ID |
| 5 | 48 | PN | R |  |  | Patient Name | Name |
| 6 | 30 | ST |  |  |  | Mother's Maiden Name | Mother’s maiden name |
| 7 | 26 | TS |  |  |  | Date of Birth | Date of birth |
| 8 | 1 | ID |  |  | 0001 | Sex | Refer to table 0001 |
| 9 | 48 | PN |  | Y |  | Patient Alias | Alias |
| 10 | 1 | ID |  |  | VA07 | Race | Race |
| 11 | 106 | AD |  | Y |  | Patient Address | Address components Component 1: Street Address (line 1) Component 2: Street Address (line 2) Component 3: City Component 4: State (abbrev.) Component 5: ZIP + 4 Component 8: Street Address (line 3) Component 9: VA County Code |
| 12 | 4 | ID |  |  |  | County Code | VA County code |
| 13 | 40 | TN |  | Y |  | Phone Number - Home | Phone number (residence) |
| 14 | 40 | TN |  | Y |  | Phone Number - Business | Phone number (work) |
| 15 | 25 | ST |  |  |  | Language - Patient | Not used |
| 16 | 1 | ID |  |  | 0002 | Marital Status | Refer to table 0002 |
| 17 | 3 | ID |  |  | VA08 | Religion | Religion |
| 18 | 20 | CK |  |  |  | Patient Account Number | Not used |
| 19 | 16 | ST |  |  |  | SSN Number - Patient | Social security number and pseudo-indicator |
| 20 | 25 | CM |  |  |  | Driver's Lic Num - Patient | Not used |
| 21 | 20 | CK |  |  |  | Mother's Identifier | Not used |
| 22 | 1 | ID |  |  | 0189 | Ethnic Group | Not used |
| 23 | 25 | ST |  |  |  | Birth Place | Not used |
| 24 | 2 | ID |  |  |  | Multiple Birth Indicator | Not used |
| 25 | 2 | NM |  |  |  | Birth Order | Not used |
| 26 | 3 | ID |  | Y | 0171 | Citizenship | Not used |
| 27 | 60 | CE |  |  | 0172 | Veterans Military Status | Not used |
| 28 | 80 | CE |  |  | 0212 | Nationality | Not used |
| 29 | 26 | TS |  |  |  | Patient Death Date and Time | Date of Death |
| 30 | 1 | ID |  |  | 0136 | Patient Death Indicator | 'Y' if Date of Death exists |

Figure 8: HL7 Patient Identification Segment (PID)

### PD1	—	Patient Demographic

| SEQ | LEN | DT | R/O | RP/# | TBL# | Item# | Element Name | VISTA Element NAME |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | ID | O | Y | 0223 | 00755 | Living Dependency | Not used |
| 2 | 2 | ID | O |  | 0220 | 00742 | Living Arrangement | Not used |
| 3 | 90 | XON | O | Y |  | 00756 | Patient Primary Facility | Component 1: CIRN Master of Record Component 2: Not Used Component 3: VA Station Number |
| 4 | 90 | XCN | O | Y |  | 00757 | Patient Primary Care Provider Name & ID No. | Not used |
| 5 | 2 | ID | O |  |  | 00758 | Student Indicator | Not used |
| 6 | 2 | ID | O |  |  | 00753 | Handicap | Not used |
| 7 | 2 | ID | O |  |  | 00759 | Living Will | Not used |
| 8 | 2 | ID | O |  |  | 00760 | Organ Donor | Not used |
| 9 | 2 | ID | O |  |  | 00761 | Separate Bill | Not used |
| 10 | 2 | CM | O | Y |  | 00762 | Duplicate Patient | Not used |
| 11 | 1 | CE | O |  | 0125 | 00743 | Publicity Indicator | Not used |
| 12 | 1 | ID | O |  | 01293 | 01283 | Protection Indicator | Not used |

Figure 9: HL7 Patient Demographic (PD1)

| ZPD — VA specific Patient Information Segment |
| --- |
| SEQ | LEN | DT | R/O | RP/# | TBL# | VISTA Element Name |
| 1 | 4 | SI | R |  |  | Set ID - Patient ID |
| 2 | 60 | ST |  |  |  | Remarks |
| 3 | 20 | ST |  |  |  | Place of Birth City |
| 4 | 2 | ST |  |  |  | Place of Birth State |
| 5 | 2 | ID |  |  | VA02 | Current Means Test Status |
| 6 | 35 | ST |  |  |  | Father's Name |
| 7 | 35 | ST |  |  |  | Mother's Name |
| 8 | 1 | ID |  |  | VA01 | Rated Incompetent |
| 9 | 19 | TS |  |  |  | Date of Death |
| 10 | 48 | PN |  |  |  | Collateral Sponsor |
| 11 | 1 | ID |  |  | VA01 | Active Health Insurance? |
| 12 | 1 | ID |  |  | VA01 | Covered by Medicaid? |
| 13 | 19 | TS |  |  |  | Date Medicaid Last Asked |
| 14 | 1 | ID |  |  | VA07 | Race |
| 15 | 3 | ID |  |  | VA08 | Religion |
| 16 | 1 | ID |  |  | VA01 | Homeless Indicator |
| 17 | 1 | ST |  |  |  | POW Status Indicated? |
| 18 | 2 | ID |  |  | VA12 | Type of Insurance |
| 19 | 1 | ID |  |  | VA14 | MECIDATION COPAYMENT EXCEMPTION |
| 20 | 22 | CE |  |  | VA23 | PRISONER OF WAR LOCATION |
| 21 | 30 | ST |  |  |  | PRIMARY CARE TEAM |

Figure 10: HL7 VA specific Patient Information Segment (ZPD)

| PV1 — Patient Visit Segment |
| --- |
| SEQ | LEN | DT | R/O | RP/# | TBL# | Element Name | VISTA Element Name |
| 1 | 4 | SI |  |  |  | Set ID - Patient Visit | Sequential Number |
| 2 | 1 | ID | R |  | 0004 | Patient Class | O= outpatient I= inpatient |
| 3 | 12 | CM |  |  |  | Assigned Patient Location | Not used |
| 4 | 4 | ID |  |  |  | Admission Type | Not used |
| 5 | 20 | ST |  |  |  | Preadmit Number | Not used |
| 6 | 12 | CM |  |  |  | Prior Patient Location | Not used |
| 7 | 60 | CN |  |  | 0010 | Attending Doctor | Not used |
| 8 | 60 | CN |  |  | 0010 | Referring Doctor | Not used |
| 9 | 60 | CN |  | Y | 0010 | Consulting Doctor | Not used |
| 10 | 3 | ID |  |  | 0069 | Hospital Service | Not used |
| 11 | 12 | CM |  |  |  | Temporary Location | Not used |
| 12 | 2 | ID |  |  | 0087 | Preadmit Test Indicator | Not used |
| 13 | 2 | ID |  |  | 0092 | Readmission Indicator | Not used |
| 14 | 3 | ID |  |  | 0023 | Admit Source | Refer to table 0023 (Location of Visit) |
| 15 | 2 | ID |  | Y | 0009 | Ambulatory Status | Not used |
| 16 | 2 | ID |  |  | 0099 | VIP Indicator | Not used |
| 17 | 60 | CN |  |  | 0010 | Admitting Doctor | Not used |
| 18 | 2 | ID |  |  | 0018 | Patient Type | Not used |
| 19 | 15 | NM |  |  |  | Visit Number | Pointer to entry in OUTPATIENT ENCOUNTER file |
| 20 | 50 | CM |  | Y | 0064 | Financial Class | Not used |
| 21 | 2 | ID |  |  | 0032 | Charge Price Indicator | Not used |
| 22 | 2 | ID |  |  | 0045 | Courtesy Code | Not used |
| 23 | 2 | ID |  |  | 0046 | Credit Rating | Not used |
| 24 | 2 | ID |  | Y | 0044 | Contract Code | Not used |
| 25 | 8 | DT |  | Y |  | Contract Effective Date | Not used |
| 26 | 12 | NM |  | Y |  | Contract Amount | Not used |
| 27 | 3 | NM |  | Y |  | Contract Period | Not used |
| 28 | 2 | ID |  |  | 0073 | Interest Code | Not used |
| 29 | 1 | ID |  |  | 0110 | Transfer to Bad Debt Code | Not used |
| 30 | 8 | DT |  |  |  | Transfer to Bad Debt Date | Not used |
| 31 | 10 | ID |  |  | 0021 | Bad Debt Agency Code | Not used |
| 32 | 12 | NM |  |  |  | Bad Debt Transfer Amount | Not used |
| 33 | 12 | NM |  |  |  | Bad Debt Recovery Amount | Not used |
| 34 | 1 | ID |  |  | 0111 | Delete Account Indicator | Not used |
| 35 | 8 | DT |  |  |  | Delete Account Date | Not used |
| 36 | 3 | ID |  |  | 0112 | Discharge Disposition | Not used |
| 37 | 25 | CM |  |  | 0113 | Discharged to Location | Not used |
| 38 | 2 | ID |  |  | 0114 | Diet Type | Not used |
| 39 | 7 | ID |  |  | 0115 | Servicing Facility | Not used |
| 40 | 1 | ID |  |  | 0116 | Bed Status | Not used |
| 41 | 2 | ID |  |  | 0117 | Account Status | Not used |
| 42 | 12 | CM |  |  |  | Pending Location | Not used |
| 43 | 12 | CM |  |  |  | Prior Temporary Location | Not used |
| 44 | 26 | TS |  |  |  | Admit Date/Time | Date/time of encounter |
| 45 | 26 | TS |  |  |  | Discharge Date/Time | Not used |
| 46 | 12 | NM |  |  |  | Current Patient Balance | Not used |
| 47 | 12 | NM |  |  |  | Total Charges | Not used |
| 48 | 12 | NM |  |  |  | Total Adjustments | Not used |
| 49 | 12 | NM |  |  |  | Total Payments | Not used |
| 50 | 20 | CM |  |  |  | Alternate Visit ID | Unique Identifier (PCE) |
| 51 | 1 | IS |  |  | 0326 | Visit Indicator | Not used |
| 52 | 60 | XCN |  | Y | 0010 | Other Healthcare Provider | Not used |

Figure 11: HL7 Patient Visit Segment (PV1)

### MRG	—	Merge Patient Information

| SEQ | LEN | DT | R/O | RP# | TBL# | Item# | Element Name | Vista Element Name |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 20 | CM | R |  |  | 00211 | Prior Patient ID - Internal | ICN |
| 2 | 16 | ST |  |  |  | 00212 | Prior Alternate Patient ID |  |
| 3 | 20 | CK |  |  |  | 00213 | Prior Patient Account Number |  |
| 4 | 16 | CK |  |  |  | 00214 | Prior Patient ID - External |  |
| 5 | 20 | CX |  |  |  | 01279 | Prior Visit Number |  |
| 6 | 20 | CX |  |  |  | 01280 | Prior Alternate Visit |  |
| 7 | 48 | XPN |  |  |  | 01281 | Prior Patient Name |  |

Figure 12: HL7 Merge Patient Information (MRG)

### MFI	—	Master File Identification Segment

| SEQ | LEN | DT | R/O | RP# | TBL# | Element Name | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 60 | CE | R | N | 0175 | Master File Identifier | 'TFL' for Treating Facility updates |
| 2 | 180 | HD | O |  | 0176 | Master File Application Identifier | Not used |
| 3 | 3 | ID | R |  | 0178 | File-Level Event Code | 'REP' or 'UPD' |
| 4 | 26 | TS | O |  |  | Entered Date/Time | Not used |
| 5 | 26 | TS | O |  |  | Effective Date/Time | Not used |
| 6 | 2 | ID | R |  | 0179 | Response Level Code | 'NE' |
| 7 | 20 | ST |  |  |  | Facility | Component 1: Station Number Component 2: Facility Name |

Figure 13: HL7 Master File Identification Segment (MFI)

### MFE	—	Master File Entry Segment

| SEQ | LEN | DT | R/O | RP# | TBL# | Element Name | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 3 | ID | R |  | 0180 | Record-Level Event Code | 'MAD' for Treating Facility updates |
| 2 | 20 | ST | C |  |  | MFN Control ID | Not used |
| 3 | 26 | TS |  |  |  | Effective Date/Time | Date Last Treated from file 391.91 Treating Facility List |
| 4 | 60 | CE | R | Y |  | Primary Key Value | For Treating Facility updates: Component 1: Station Number Component 2: Institution Name Component 3: 'VA' Component 4: ICN Component 5: 'ICN' Component 6: 'VA' |

Figure 14: HL7 Master File Entry Segment (MFE)

### VTQ	—	 Attributes

| SEQ | LEN | DT | OPT | RP/# | TBL# | Item# | Element Name | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 32 | ST | O |  |  | 00696 | Query Tag | Sequence Number identifier |
| 2 | 1 | ID | R |  | 0106 | 00697 | Query/Response Format Code | See Table 0106: CIRN V.1.0 uses only 'T' |
| 3 | 60 | CE | R |  |  | 00698 | VT Query Name | See table VA-13 VT Query Name |
| 4 | 60 | CE | R |  |  | 00699 | Virtual Table Name | Logical name (i.e., ICN) |
| 5 | 256 | QSC | O | Y |  | 00700 | Selection Criteria | Qualifier field Name (see Table VA-14 VTQ Selection Criteria) Relational Operator (see Table 0209) Relational Conjunction (see Table 0210) |

Figure 15: HL7 Attributes (VTQ)

### RDF	—	Table Row Definition Segment

| SEQ | LEN | DT | OPT | RP/# | TBL# | Item# | Element Name | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 3 | NM | R |  |  | 00701 | Number of Columns per Row | Number of data elements to be returned |
| 2 | 40 | RCD | R | Y |  | 00702 | Column Description | Component 1: HL7 Field Number Component 2: Data Type Component 3: Max. length |

Figure 16: HL7 Table Row Definition Segment (RDF)

### RDT	—	Table Row Data Segment

| SEQ | LEN | DT | OPT | RP/# | TBL# | Item# | Element Name | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1-n | Variable | Variable | R |  |  | 00703 | Column Value | Actual data found |

Figure 17: HL7 Table Row Data Segment (RDT)

### ZEL	—	VA specific Patient Eligibility Segment

| SEQ | LEN | DT | R/O | RP/# | TBL# | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 4 | SI | R |  |  | SET ID |
| 2 | 2 | ID |  |  | VA04 | Eligibility code |
| 3 | 16 | CK |  |  |  | Long ID |
| 4 | 12 | ST |  |  |  | Short ID |
| 5 | 1 | ID |  |  | VA05 | Disability Retirement From Mil. |
| 6 | 8 | NM |  |  |  | Claim folder number |
| 7 | 40 | ST |  |  |  | Claim folder location |
| 8 | 1 | ID |  |  | VA01 | Veteran? |
| 9 | 30 | ST |  |  |  | Type of patient |
| 10 | 1 | ID |  |  | VA06 | Eligibility Status |
| 11 | 8 | DT |  |  |  | Eligibility Status Date |
| 12 | 8 | DT |  |  |  | Eligibility Interim Response |
| 13 | 50 | ST |  |  |  | Eligibility Verification Method |
| 14 | 1 | ID |  |  | VA01 | RECEIVING A&A BENEFITS? |
| 15 | 1 | ID |  |  | VA01 | RECEIVING HOUSEBOUND BENEFITS? |
| 16 | 1 | ID |  |  | VA01 | RECEIVING A VA PENSION? |
| 17 | 1 | ID |  |  | VA01 | RECEIVING A VA DISABILITY? |
| 18 | 1 | ID |  |  | VA01 | EXPOSED TO AGENT ORANGE |
| 19 | 1 | ID |  |  | VA01 | RADIATION EXPOSURE INDICATED |
| 20 | 1 | ID |  |  | VA01 | ENVIRONMENTAL CONTAMINANTS |
| 21 | 5 | NM |  |  | VA01 | TOTAL ANUAL VA CHECK AMOUNT |
| 22 | 22 | CE |  |  | VA0122 | RADIATION EXPOSURE METHOD |

Figure 18: HL7 VA specific Patient Eligibility Segment (ZEL)

### ZSP	—	VA specific Service Period Segment

| SEQ | LEN | DT | R/O | RP/# | TBL# | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 4 | SI | R |  |  | Set ID |
| 2 | 1 | ID | R |  | VA01 | Service Connected? |
| 3 | 3 | NM |  |  |  | Service Connected Percentage |
| 4 | 2 | ID |  |  | VA11 | Period of Service |
| 5 | 1 | ST |  |  |  | Vietnam Service Indicated? |

Figure 19: HL7 VA specific Service Period Segment (ZSP)

### ZCT	—	VA Specific Emergency Contact Segment

| SEQ | LEN | DT | R/O | RP/# | TBL# | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 4 | SI | R |  |  | Set ID |
| 2 | 1 | ID |  |  | VA01 | Next of Kin (NOK) |
| 3 | 35 | ST |  |  |  | Name of NOK |
| 4 | 30 | ST |  |  |  | Relationship of NOK |
| 5 | 106 | AD |  | Y |  | Component 1:K-Street Address (line 1) Component 2:K-Street Address (line 2) & K-Street Address (line 3) Component 3:K-City Component 4: K-State (abbreviation) Component 5: K-ZIP code |
| 6 | 40 | TN |  | Y |  | K-Phone Number |
| 7 | 40 | TN |  | Y |  | K-Work phone number |
| 8 | 1 | ID |  |  | VA01 | Contact address same as NOK? |
| 9 | 1 | ID |  |  | VA01 | Contact person same as NOK? |

Figure 20: HL7 VA Specific Emergency Contact Segment (ZCT)

### ZEM	—	VA Specific Employment Information Segment

| SEQ | LEN | DT | R/O | RP/# | TBL# | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 4 | SI | R |  |  | SET ID |
| 2 | 1 | ID |  |  | VA01 | Patient Data Requested? |
| 3 | 1 | ID |  |  | VA15 | Employment Status |
| 4 | 30 | ST |  |  |  | Employer Name |
| 5 | 30 | ST |  |  |  | Occupation |
| 6 | 106 | AD |  | Y |  | Component 1: Employer Street (line 1) Component 2: Employer Street (line 2 & line 3) Component 3: Employer City Component 4: Employer State Component 5: Employer ZIP Code |
| 7 | 40 | TN |  | Y |  | Employer Phone number |
| 8 | 1 | ID |  |  | VA01 | Government Agency? |

Figure 21: HL7 VA Specific Employment Information Segment (ZEM)

### ZFF	—	VA Specific File/Field Segment

| SEQ | LEN | DT | R/O | RP/# | TBL# | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 20 | NM | R |  |  | File Number |
| 2 | 150 | ST | R |  |  | Field Number(s) |

Figure 22: HL7 VA Specific File/Field Segment (ZFF)

### OBX	—	Observation/Result Segment

| SEQ | LEN | DT | R/O | RP/# | TBL# | Item# | Element Name | VISTA Element Name |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 10 | SI | O |  |  | 00569 | Set ID - OBX | Not used |
| 2 | 2 | ID | C |  | 0125 | 00570 | Value Type | CE |
| 3 | 590 | CE | R |  |  | 00571 | Observation Identifier | 38.1^SECURITY LOG |
| 4 | 20 | ST | C |  |  | 00572 | Observation Sub-ID | Not used |
| 5 | 65536 | * | C | Y |  | 00573 | Observation Value | Sensitive= 1 Not Sensitive or No Value= 0 |
| 6 | 60 | CE | O |  |  | 00574 | Units | Not used |
| 7 | 10 | ST | O |  |  | 00575 | References Range | Not used |
| 8 | 5 | ID | O | Y/5 | 0078 | 00576 | Abnormal Flags | Not used |
| 9 | 5 | NM | O |  |  | 00577 | Probability | Not used |
| 10 | 2 | ID | O | Y | 0080 | 00578 | Nature of Abnormal Test | Not used |
| 11 | 1 | ID | R |  | 0085 | 00579 | Observ Result Status | R=Results entered, Not verified |
| 12 | 26 | TS | O |  |  | 00580 | Date Last Obs Normal Values | Not used |
| 13 | 20 | ST | O |  |  | 00581 | User Defined Access Checks | Not used |
| 14 | 26 | TS | O |  |  | 00582 | Date/Time of the Observation | Date if found in VISTA |
| 15 | 60 | CE | O |  |  | 00583 | Producer"s ID | Not used |
| 16 | 80 | XCN | O |  |  | 00584 | Responsible Observer | Name if found in VISTA |
| 17 | 60 | CE | O | Y |  | 00936 | Observation Method | Not used |

Figure 23: HL7 Observation/Result Segment (OBX)

# Unsolicited HL7 Messages

## Trigger Events and Message Definitions Broadcast to Sites and to the MPI

Listed below is a compilation of the trigger events and the corresponding HL7 message that the MPI package generates or is interested in. The notation used to describe the sequence, optionally, and repetition of segments are described in the HL7 manual, Chapter 2, "Format for Defining Abstract Messages."

### ADT A04 Message — Register a Patient

This event is only triggered after the successful completion of a Patient Registration using the Registration menu options Register a Patient. This message is currently broadcast real-time. The example below constitutes a PIMS-generated HL7 message.

| Abbreviated Name | Full Name |
| --- | --- |
| MSH | Message Header |
| EVN | Event Type |
| PID | Patient Identification |
| PD1 | Additional Demographics |
| PV1 | Patient Visit |
| OBX | Observation/Result |
| ZPD | VA-Specific Patient Information |
| ZSP | VA Specific Service Period |
| ZEL | VA Specific Eligibility Information |
| ZCT | VA Specific Emergency Contact Information |
| ZEM | VA Specific Employment Information |
| ZFF | VA Specific File/Field |

Figure 24: HL7 ADT A04 message type (Register a Patient)

Sample message:

MSH^~|\&^VAFC PIMS^573^RG CIRN^573^19980624091752^^ADT~A04^4556986^P^2.3^

^^NE^NE^USA

EVN^A04^199809040911^^^12564~DOE~JANE

PID^1^1000646385V533117^7169807~8~M10^5678^SMITH~HERMAN~FRANK^""^19680702^M^^^""~""~""~""~""~~~""~""^^""^""^^M^0^^000045678^^^^^^^^^^

PD1^^^ALBANY, NY~~500^""

PV1^1^O^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^2980904.0911

OBX^^CE^38.1~SECURITY LOG^^N~NO~HL70136^^^^^^R^^^""^^""

ZPD^1^""^""^""^""^""^""^""^""^""^0^""^""^""^0^^^^^^

ZSP^1^1^^""^""^""^""

ZEL^1^""^""^""^""^""^""^1^SC VETERAN^""^""^""^^^^^^^^

ZCT^1^1^""^""^""^""^""^""^""

ZEM^1^1^1^US MARINE CORP^""^""^""^""

ZFF^2^.01;.02;.03;.05;.08;.09;.301;.31115;1901;391;

Figure 25: Sample HL7 ADT A04 message (Register a Patient)

### ADT A08 Message — Update Patient Information

The event of updating patient information can take place from several different options within VISTA, including VA FileMan. Changes to any of the fields listed below will be recorded and an entry created in the HL7/ADT Pivot file and the entry will be marked as needing to be transmitted. Direct sets to the globals cannot be collected. A background job will periodically collect (via a scheduled job) these marked events and broadcast an ADT-A08 Update Patient Information message.

Because it is not possible to determine if the editing of the patient's data has been completed, a background job [VAFC BATCH UPDATE] will periodically collect these marked events and broadcast the appropriate A08 message. This is a PIMS-generated HL7 message.

In the DG SECURITY LOG file (#38.1), Field #2 Security Level is monitored for changes to patient sensitivity. The following data elements are currently being monitored in the PATIENT file (file #2) for changes.

| Field Number | Field Name |
| --- | --- |
| .01 | NAME |
| .02 | SEX |
| .03 | DATE OF BIRTH |
| .05 | MARITAL STATUS |
| .08 | RELIGIOUS PREFERENCE |
| .09 | SOCIAL SECURITY NUMBER |
| .111 | STREET ADDRESS |
| .112 | STREET ADDRESS [2] |
| .114 | CITY |
| .115 | STATE |
| .1112 | ZIP+4 |
| .117 | COUNTY |
| .301 | SERVICE CONNECTED |
| .302 | SERVICE CONNECTED PERCENTAGE |
| .31115 | EMPLOYMENT STATUS |
| .323 | PERIOD OF SERVICE |
| .361 | PRIMARY ELIGIBILITY CODE |
| 391 | PATIENT TYPE |
| 1901 | VETERAN (Y/N) |
| .351 | DATE OF DEATH |
| .2403 | MOTHER'S MAIDEN NAME |
| .131 | PHONE NUMBER [RESIDENCE] |
| .132 | PHONE NUMBER [WORK] |
| .219 | K-PHONE NUMBER |
| .211 | K-NAME |
| 991.01 | INTEGRATION CONTROL NUMBER |

Figure 26: Data elements monitored in the PATIENT file (file #2) for changes

| Abbreviated Name | Full Name |
| --- | --- |
| MSH | Message Header |
| EVN | Event Type |
| PID | Patient Identification |
| PD1 | Additional Demographics |
| PV1 | Patient Visit |
| OBX | Observation/Result |
| ZPD | VA-Specific Patient Information |
| ZSP | VA Specific Service Period |
| ZEL | VA Specific Eligibility Information |
| ZCT | VA Specific Emergency Contact |
| ZEM | VA Specific Employment Information |
| ZFF | VA Specific File/Field |

Figure 27: HL7 ADT A08 message type (Update Patient Information)

Sample message:

MSH^~|\&^VAFC PIMS^546^RG CIRN^^19980624095305^^ADT~A08^1932761^P^2.3^

^^NE^NE^USA

EVN^A08^19980624^^^JONES,SALLY

PID^1^500000021V980613^227~1~M10^8888^JONES~BEAVER~I^DAD^19540913^M^^3^RIVER ROAD~TESTING~ALBANY~AK~25244~~~MORE TESTING~110^110^""^""^^M^29^

^000058888^^^^^^^^^^19970825^Y

PD1^^^ALBANY, NY~~500^""

PV1^1^O^""^^^^^^^^^^^^^^^NSC VETERAN^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^^13898

OBX^^CE^38.1~SECURITY LOG^^N~NO~HL70136^^^^^^R^^^""^^""

ZPD^1^[PATIENT DIED ON 08/25/97]^NEW YO{K^NY^""^""^""^""^19970825^""^1^1^

198605281632^^^""^N^1^^^

ZSP^1^1^50^X^""^""^""

ZEL^1^1^222-55-8888~8~M10^8888^""^""^""^1^NSC VETERAN^V^19970603^""^""^^^^

^^^

ZCT^1^1^TEST^""^""^""^""^""^""

ZEM^1^1^9^""^""^""^""^""

ZFF^2^.01;

Figure 28: Sample HL7 ADT A08 message (Update Patient Information)

### ADT A28 Message — Adding a New Patient

When a Direct Connect query is made to the MPI and no matches are found for that patient, a request is sent that this patient be added to the MPI. This message is generated specifically for the CIRN and MPI applications.

| Abbreviated Name | Full Name |
| --- | --- |
| MSH | Message Header |
| EVN | Event Type |
| PID | Patient Identification |
| PD1 | Additional Demographics |
| PV1 | Patient Visit |
| OBX | Observation/Result |
| ZPD | VA-Specific Patient Information |
| ZSP | VA-Specific Service Period |
| ZEL | VA-Specific Eligibility Information |
| ZCT | VA Specific Emergency Contact Information |
| ZEM | VA Specific Employment Information |

Figure 29: HL7 ADT A28 message type (Adding a New Patient)

Sample message:

MSH^~|\&^VAFC PIMS^500^MPI^200M^^^ADT~A28^^P^2.3^^^NE^NE^USA

EVN^A28^19980904^^94^SMITH,HERMAN O

PID^1^""^7169808~9~M10^4890^ADAMS~JOHN~O^""^19330920^M

^^7^""~""~""~""~""~~~""~""^^""^""^^""^29^^000034890^^^^^^^^^^

PD1^^^ALBANY, NY~~500^""

PV1^1

OBX^^CE^38.1~SECURITY LOG^^N~NO~HL70136^^^^^^R^^^""^^""

ZPD^1^""^""^""^""^""^""^""^""^""^0^""^""^^^""^""^0^^^

ZSP^1^1^^""^""^""^""

ZEL^1^""^""^""^""^""^""^1^SC VETERAN^""^""^""^""^^^^^^^

ZCT^1^1^""^""^""^""^""^""^""

ZEM^1^1^""^""^""^""^""^""

Figure 30: Sample HL7 ADT A28 message (Adding a New Patient)

### ADT A29 Message — Delete Person Information

An A29 event can be used to delete demographic information related to a given person. The fields, included when this message is sent, should be only the fields necessary to communicate this event. When other important fields change, it is recommended that the A08-Update event be used instead. Only the CMOR can trigger the A29 message to the MPI. In addition, the patient cannot have any other subscribers.

| Abbreviated Name | Full Name |
| --- | --- |
| MSH | Message Header |
| EVN | Event Type |
| PID | Patient Identification |
| PD1 | Additional Demographics |
| PV1 | Patient Visit |

Figure 31: HL7 ADT A29 message type (Delete Person Information)

Sample message:

MSH^~|\&^MPI A29 SERVER^662^MPI^MPI^19980817063410^^

ADT~A29^192^P^2.3^^^NE^AL^|

EVN^A29^2980817.06341^^^

PID^^1000310536V304686^247~7~M10^^DOE~JOHNNY^^^^^^^^^^^^^^^^^^^^^^^^

Figure 32: Sample HL7 ADT A29 message (Delete Person Information)

### ADT A30 Message — Merge Person Information

An A30 event is used to correct the ICN for a given patient. This message will be sent to all sites that know about the "incorrect ICN" and the MPI. The "incorrect ICN" identified on the MRG segment (MRG-1) is to be merged with the "correct ICN" identified on the PID segment (PID-3). The "incorrect ICN" then is placed in the ICN History multiple. The site initiating the Merge message must be the CMOR of both patients. The message is sent to all sites that know the patients and to the MPI.

The A30 event is not being used to "merge" patient records, but to change the ICN.

| Abbreviated Name | Full Name |
| --- | --- |
| MSH | Message Header |
| EVN | Event Type |
| PID | Patient Identification |
| PD1 | Additional Demographics |
| PV1 | Patient Visit |
| MRG | Merge Information |

Figure 33: HL7 ADT A30 message type (Merge Person Information)

Sample message:

MSH^~|\&^MPI A30 SERVER^662^MPI^MPI^19980723104335^

^ADT~A30^163^P^2.3^^^NE^AL^USA|

EVN^A30^2980723.104335^^^

PID^1^1000646316V698194^249~3~M10^3890^DOE~JOHN^""^19680702^M^^7^200 SYCAMORE ST~""~JACKSONVILLE~NC~28546~~~""~133^133^""^""^^^29^

^000023890^^^^^^^^^^

MRG^1000646317

Figure 34: Sample HL7 ADT A30 message (Merge Person Information)

### MFN — Update Treating Facility

A treating facility list is a list of medical centers where the veteran has been seen. If this list is updated through the appropriate APIs, this event will be added to the ADT/HL7 Pivot file and marked for transmission. A background job will then collect the events and broadcast an MFN message. Direct sets to the Treating Facility List global will not trigger this event. This is a PIMS-generated HL7 message that was designed for CIRN/MPI.

| Abbreviated Name | Full Name |
| --- | --- |
| MSH | Message Header |
| MFI | Master File Identification Segment |
| MFE | Master File Entry Segment |

Figure 35: HL7 Update Treating Facility message type (MFN)

A Master File Treating Facility Update message can be generated either by a patient’s primary facility (CMOR) or from a non-owner (non-CMOR). If it is generated from the owner, the MFI segment will be different.

(From Owner) In this case, sequence number 3 "File-level event code" will contain "REP." This indicates that the receiving application should replace their Treating Facility List with what is in the message. This message is sent to the MPI and any other treating facilities that share this patient.

Sample message:

MSH^~|\&^VAFC PIMS^573^VAFC PIMS^573^19980702163006^^MFN~M05^3858303^P^

2.3^^^NE

^NE^USA|

MFI^TFL^^REP^^^NE^573~GAINESVILLE

MFE^MAD^^19980702^573~GAINESVILLE~VA~1000321432~ICN~VA

MFE^MAD^^19980702^673~TAMPA, FL~VA~1000321432~ICN~VA

Figure 36: Sample HL7 Update Treating Facility (MFN) message from Owner

(From Non-owner) In this case, sequence number 3 will contain "UPD." This indicates to the receiving application that the information in the message should be added to their current list. This message is only sent to the CMOR.

Sample message:

MSH^~|\&^VAFC PIMS^673^VAFCPIMS^673^19980702163006^^MFN~M05^3858303^P^2.3^

^^NE^NE^USA|

MFI^TFL^^UPD^^^NE^573~GAINVILLE

MFE^MAD^^19980702^673~TAMPA, FL~VA~1000321432~ICN~VA

Figure 37: Sample HL7 Update Treating Facility (MFN) message from Non–owner

### VQQ — Virtual Table Query (Event Q01)

| Abbreviated Name | Full Name |
| --- | --- |
| MSH | Message Header |
| VTQ | VTQ Definition |
| RDF | Table Row Definition |
| RDT | Table Row Data Segment |

Figure 38: HL7 Virtual Table Query (VQQ) message type — Event Q01

The MPI VISTA software utilizes the HL7 item numbers from the HL7 V. 2.3 Standard to identify the fields in a VTQ segment. A VTQ segment in the HL7 2.3 standard is used to address the needs of adding and identifying patients to the MPI.

The VQQ message is utilized during the Initialization process and resolution of Local and Missing ICNs in a batch message. It is also used during the Direct Connect functionality to query the MPI in real-time.

Sample of Batch Initialization Message to the MPI:

BHS^~|\&^MPI-STARTUP^573^MPI^MPI^19980522111248^^~P~VTQ|Q02~2.3^^3689580^

MSH^~|\&^MPI-STARTUP^573^^^^^VTQ~Q02^3358741-1^P^2.3^^^NE^AL|

VTQ^513598^T^VTQ_PID_ICN_LOAD_1^ICN^@00108.1~EQ~SMITH SR.~AND|@00122~EQ~266568187~AND|@00108.2~EQ~WILLIAM~AND|@00110~EQ~19400110~

AND|@00111~EQ~M~AND|@00126.1~EQ~WINTERHAVEN~AND|@00126.2~EQ~12

RDF^9^@00108.1~ST~16|@00122~ST~9|@00110~TS~8|@00756~ST~30|@00105~ST~19|@00108.2

~ST~16|@00169~ST~30|@00740~TS~8|@00108.3~ST~16

MSH^~|\&^MPI-STARTUP^573^^^^^VTQ~Q02^3358741-2^P^2.3^^^NE^AL|

VTQ^7227887^T^VTQ_PID_ICN_LOAD_1^ICN^@00108.1~EQ~KEARNEY~AND|@00122~EQ~252247315~AND|@00108.2~EQ~JONES~AND|@00110~EQ~19240921~AND|@00111~EQ~M~AND|@00126.1~EQ~GOOD~AND|@00126.2~EQ~13

RDF^9^@00108.1~ST~16|@00122~ST~9|@00110~TS~8|@00756~ST~30|@00105~ST~19|@00108.2

~ST~16|@00169~ST~30|@00740~TS~8|@00108.3~ST~16

MSH^~|\&^MPI-STARTUP^573^^^^^VTQ~Q02^3358741-3^P^2.3^^^NE^AL|

VTQ^7246248^T^VTQ_PID_ICN_LOAD_1^ICN^@00108.1~EQ~SCHNEIDER~AND|@00122~EQ~360039771~AND|@00108.2~EQ~CLIFFORD~AND|@00110~EQ~19210820~AND|@00111~EQ~M~AND|@00126.2~EQ~29|

RDF^9^@00108.1~ST~16|@00122~ST~9|@00110~TS~8|@00756~ST~30|@00105~ST~19|@00108.2

~ST~16|@00169~ST~30|@00740~TS~8|@00108.3~ST~16

MSH^~|\&^MPI-STARTUP^573^^^^^VTQ~Q02^3358741-4^P^2.3^^^NE^AL|

VTQ^85368^T^VTQ_PID_ICN_LOAD_1^ICN^@00108.1~EQ~TURNER~AND|@00122~EQ~315543066~AND|@00108.2~EQ~LARRY~AND|@00110~EQ~19500404~AND|@00111~EQ~M~AND|@00126.1~EQ~LONDON~AND|@00126.2~EQ~21

RDF^9^@00108.1~ST~16|@00122~ST~9|@00110~TS~8|@00756~ST~30|@00105~ST~19|@00108.2

~ST~16|@00169~ST~30|@00740~TS~8|@00108.3~ST~16

BTS^4

Figure 39: Sample HL7 Virtual Table Query (VQQ) message — Event Q01 (MPI Batch Initialization)

Sample of a Direct Connect VQQ query:

MSH|^~\&|MPI_LOAD|673|MPI-ICN||||VTQ^Q02|7307018-1|

VTQ|7307018|T|VTQ_PID_ICN|ICN|@00108.1^EQ^WHEELER^AND~@00122^EQ^578160290^AND~@00108.2^EQ^HARRY^AND~@00110^EQ^19160605

RDF|9|@00108.1^ST^16~@00122^ST^9~@00110^TS^8~@00756^ST^30~@00105^ST^19~@00108.2^ST^16~@00169^ST^30~@00740^TS^8~@00108.3^ST^16^

Figure 40: Sample HL7 Virtual Table Query (VQQ) message — Event Q01 (Direct Connect Query)

## Trigger Events and Message Definitions Received

### VQQ — Virtual Table Query Response

| Abbreviated Name | Full Name |
| --- | --- |
| MSH | Message Header |
| MSA | Message Acknowledgement |
| QAK | Query Acknowledgement |
| RDF | Table Row Definition |
| RDT | Table Row Data Segment |

Figure 41: HL7 Virtual Table Query Response (VQQ) message type

The MPI VISTA software, utilizes the HL7 item numbers from the HL7 V. 2.3 Standard to identify the fields in a VTQ segment. A VTQ segment in HL7 2.3 standard is used to address the needs of adding and identifying patients' to the MPI.

Sample message that MPI Austin returns in response to an Initialization Message:

BHS^~|\&^MPI^MPI^MPI-STARTUP^^19980522114545^^~P~ACK|Q02~2.3^AA^3689580

^3689580

MSH^~|\&^MPI^MPI^MPI-STARTUP^573^^^ACK^3358741-1^P^2.3|

MSA^AA^3358741-1

QAK^513598^OK

RDF^9^@00108.1~ST~16|@00122~ST~9|@00110~TS~8|@00756~ST~30|@00105~ST~19|@00108.2~ST~16|@00169~ST~30|@00740~TS~8|@00108.3~ST~16

RDT^JONES SR.^266568187^19400110^573^1000313417V193614^WILLIAM^573^^

MSH^~|\&^MPI^MPI^MPI-STARTUP^573^^^ACK^3358741-2^P^2.3|

MSA^AA^3358741-2

QAK^7227887^OK

RDF^9^@00108.1~ST~16|@00122~ST~9|@00110~TS~8|@00756~ST~30|@00105~ST~19|@00108.2~ST~16|@00169~ST~30|@00740~TS~8|@00108.3~ST~16

RDT^KEARNEY^252247315^19240921^573^1000313418V329176^LESTER^573^^

MSH^~|\&^MPI^MPI^MPI-STARTUP^573^^^ACK^3358741-3^P^2.3|

MSA^AA^3358741-3

QAK^7246248^OK

RDF^9^@00108.1~ST~16|@00122~ST~9|@00110~TS~8|@00756~ST~30|@00105~ST~19|@00108.2~ST~16|@00169~ST~30|@00740~TS~8|@00108.3~ST~16

RDT^SCHNEIDER^360039771^19210820^573^1000313420V403579^CLIFFORD^573^^

MSH^~|\&^MPI^MPI^MPI-STARTUP^573^^^ACK^3358741-4^P^2.3|

MSA^AA^3358741-4

QAK^85368^OK

RDF^9^@00108.1~ST~16|@00122~ST~9|@00110~TS~8|@00756~ST~30|@00105~ST~19|@00108.2~ST~16|@00169~ST~30|@00740~TS~8|@00108.3~ST~16

RDT^TURNER^315543066^19500404^573^1000313421V689904^LARRY^573^^

BTS^4

Figure 42: Sample HL7 Virtual Table Query Response (VQQ) message — MPI Batch Initialization

### ADT A31 Message — Update Person Information

After a patient is either selected or added to the MPI, outside of the initialization process, an ADT-A31 message is sent via the Direct Connect process from the MPI back to the site. This message identifies the patient and contains the newly assigned or existing ICN.

| Abbreviated Name | Full Name |
| --- | --- |
| MSH | Message Header |
| MSA | Message Acknowledgement |
| QAK | Query Acknowledgement Segment |
| RDF | Table Row Definition |
| RDT | Table Row Data Segment |

Figure 43: HL7 ADT A31 message type (Update Person Information)

Sample message:

MSH|^~\&|MPI|MPI|MPI_LOAD|516|||ADT^A31|126475-1|P|2.3

MSA|AA|126475-1

QAK|126475|OK

RDF|9|@00108.1^ST^16~@00122^ST^9~@00110^TS^8~@00756^ST^30~@00105^ST^19~@00108.2^ST^16~@00169^ST^30~@00740^TS^8~@00108.3^ST^16

RDT|CLAYTON|011528127|19611206|573|1000118458V711894|ERNEST|573||

Figure 44: Sample HL7 ADT A31 message (Update Person Information)

### ADT A31 Message — Change CIRN Master of Record (CMOR)

An A31 message is also used to update CMOR information. The options on the CIRN Master of Record (CMOR) Request menu [RGVC MGR] use the A31 event to a) request a change in CMOR (site-to-site), b) to approve or disapprove a CMOR change (site-to-site), and c) to send out the CMOR change information to subscribers.

| Abbreviated Name | Full Name |
| --- | --- |
| MSH | Message Header |
| PID | Patient Identification |
| NTE | Notes and Comments: CMOR Change Information |
| EVN | Event Type |

Figure 45: HL7 ADT A31 message type [Change CIRN Master of Record (CMOR)]

Sample of change of CMOR message to sites/MPI:

MSH^~|\&^CMOR COM RESULT^500^CMOR COM RESULT^500^199801121

61216^^ADT~A31^5^P^2.3^^^^AL^USA

PID^^14V22^1~1~M10^6677^JENNIE~JAMBIE~T.^HERMAN^19350303^M^^2^^^

^^^^^^^^^^^^^^^^

EVN^A31^2980112^100^POSTMASTER

NTE^^P^^^^^662

Figure 46: Sample HL7 ADT A31 Message [Change CIRN Master Of Record (CMOR)]

### ADT A31 Message — Batch CMOR Comparison

This is used for background job to automatically change the CMOR to the requesting site if the difference in CMOR Activity Score is greater than 80%. IT sends a message back to the requestor for those that are to be changed.

| Abbreviated Name | Full Name |
| --- | --- |
| BHS | Batch Header Segment |
| MSH | Message Header |
| PID | Patient Identification |
| EVN | Event Type |
| NTE | Notes and Comments: CMOR Change Information |
| BTS | Batch Trailer Segment |

Figure 47: HL7 ADT A31 message type (Batch CMOR Comparison)

Sample of batch message to Change CMOR — sent from Non-CMOR to CMOR:

BHS^~|\&^CMOR COMPARISON^662^CMOR COMPARISON^662

^19980209195518^^~P~ADT|A31~2.3^^33799^

MSH^~|\&^CMOR COMPARISON^594^^^^^ADT~A31^33799-1^P^2.3^^^NE^AL^USA

EVN^A31^FEB 9,1998^^COOL-JAY,L.L.

PID^^1000304658V437719^7364309~2~M10^^LAKECITY~G~ONE^^^^^^^^^^^^^^^^^^^^^^^^

NTE^COMPARISON^573

MSH^~|\&^CMOR COMPARISON^594^^^^^ADT~A31^33799-2^P^2.3^^^NE^AL^USA

EVN^A31^FEB 9,1998^^COOL-JAY,L.L.

PID^^1000304667V895694^7364323~8~M10^^LAKECITY~G~TWO^^^^^^^^^^^^^^^^^^^^^^^^

NTE^COMPARISON^573

MSH^~|\&^CMOR COMPARISON^594^^^^^ADT~A31^33799-3^P^2.3^^^NE^AL^USA

EVN^A31^FEB 9,1998^^COOL-JAY,L.L.

PID^^1000304668V520186^7364324~9~M10^^LAKECITY~GT~ONE^^^^^^^^^^^^^^^^^^^^^^^^

NTE^COMPARISON^573

BTS^3

Figure 48: Sample HL7 ADT A31 message (Batch CMOR Comparison)

# Appendix A

## HL7 Standard Tables

Table 0001 — Sex

| Value | Description |
| --- | --- |
| F | Female |
| M | Male |
| O | Other |
| U | Unknown |

Table 0002 — Marital Status (user defined)

| Value | Description |
| --- | --- |
| A | Separated |
| D | Divorced |
| M | Married |
| W | Widow/Widower |
| S | Never Married |
| U | Unknown |

Table 0003 — ADT/R Event Type Codes

| Value | Description |
| --- | --- |
| A04 ADT/ACK | Register a patient |
| A08 ADT/ACK | Update patient information |
| A28 ADT/ACK | Add person information |
| A29 ADT/ACK | Delete person information |
| A30 ADT/ACK | Merge person information |
| A31 ADT/ACK | Update person information |
| M05 MFN/MFK | Patient location master file |
| Q02 QRY/QCK | Query sent for deferred response |

Table 0008 — Acknowledgment Code

| Value | Description |
| --- | --- |
| AA | Original mode: Application Accept Enhanced mode: Application Acknowledgment: Accept |
| AE | Original mode: Application Error Enhanced mode: Application Acknowledgment: Error |
| AR | Original mode: Application Reject Enhanced mode: Application Acknowledgment: Reject |
| CA | Enhanced mode: Accept Acknowledgment: Commit Accept |
| CE | Enhanced mode: Accept Acknowledgment: Commit Error |
| CR | Enhanced mode: Accept Acknowledgment: Commit Reject |

Table 0023 — Admit Source (user defined)

Sample listing of possible values used for Location of Visit

| Value | Description |
| --- | --- |
| 1 | This facility |
| 6 | Other facility |

Table 0062 — Event Reason (user defined)

| Value | Description |
| --- | --- |
| 01 | Patient Request |
| 02 | Physician Order |
| 03 | Census Management |
| 04 | Update to Old Event |
| 05 | Update to New/Current Event |
| 97 | Sensitivity Update |
| 99 | Date of Death |

Table 0076 — HL7 Message Type

Sample of possible values

| Value | Description |
| --- | --- |
| ADT | ADT Message |
| MFN | Master File Notification |

| Table 0106 — Query/Response Format Code |
| --- |
| Value | Description |
| D | Response is in display format |
| R | Response is in record-oriented format |
| T | Response is in tabular format |

Table 0115 — Servicing Facility (user defined)

Sample of possible values

| Value | Description |
| --- | --- |
| 512 9AC | Perry Point (Nursing Home) |

| Table 0125 - Value type (new) |
| --- |
| Value | Description |
| AD | Address |
| CE | Coded Entry |
| CF | Coded Element With Formatted Values |
| CK | Composite ID With Check Digit |
| CN | Composite ID And Name |
| CP | Composite Price |
| CX | Extended Composite ID With Check Digit |
| DT | Date |
| ED | Encapsulated Data |
| FT | Formatted Text (Display) |
| MO | Money |
| NM | Numeric |
| PN | Person Name |
| RP | Reference Pointer |
| SN | Structured Numeric |
| ST | String Data. |
| TM | Time |
| TN | Telephone Number |
| TS | Time Stamp (Date & Time) |
| TX | Text Data (Display) |
| XAD | Extended Address |
| XCN | Extended Composite Name And Number For Persons |
| XON | Extended Composite Name And Number For Organizations |
| XPN | Extended Person Number |
| XTN | Extended Telecommunications Number |

Table 0136 — Patient Death Indicator

| Value | Description |
| --- | --- |
| Y | Yes |

Table 0209 — Relational Operator

| Relational Operator | Value |
| --- | --- |
| EQ | Equal |
| NE | Not Equal |
| LT | Less than |
| GT | Greater than |
| LE | Less than or equal |
| GE | Greater than or equal |
| CT | Contains |
| GN | Generic |

Table 0210 — Relational Conjunction

| Relational Conjunction | Note |
| --- | --- |
| AND | Default |
| OR |  |

Table 175 — Master File Identifier Code

| Value | Description |
| --- | --- |
| TFL | Treating Facility Master File (Local Agreement) |

Table 178 — File Level Event Code

| Value | Description |
| --- | --- |
| REP | Replace current version of this master file with the version contained in this message |
| UPD | Change file records as defined in the record level event codes for each record that follows |

Table 179 — Response Level

| Value | Description |
| --- | --- |
| NE | Never. No application-level response needed |
| ER | Error/Reject conditions only. Only MFA segments denoting errors must be returned via the application-level acknowledgment for this message |
| AL | Always. All MFA segments (whether denoting errors or not) must be returned via the application-level acknowledgment message |
| SU | Success. Only MFA segments denoting success must be returned via the application-level acknowledgment for this message |

Table 180 — Record Level Event Code

| Value | Description |
| --- | --- |
| MAD | Add record to master file |
| MDL | Delete record from master file |
| MUP | Update record for master file |
| MDC | Deactivate: discontinue using record in master file, but do not delete from database |
| MAC | Reactivate deactivated record |

## VA Specific Tables

Table VA01 — Yes/No

| Value | Description |
| --- | --- |
| 0 | NO |
| 1 | YES |

Table VA02 — Current Means Test Status

Type of Care (#.03) field of Means Test Status (#408.32) file

| Value | Description |
| --- | --- |
| D | DISCRETIONARY |
| M | MANDATORY |
| N | NOT APPLICABLE |

Table VA04 — Eligibility

Name (#.01) field of MAS Eligibility Code (#8.1) file

| Value | Description |
| --- | --- |
| 1 | SERVICE CONNECTED 50% to 100% |
| 2 | AID & ATTENDANCE |
| 3 | SC LESS THAN 50% |
| 4 | NSC - VA PENSION |
| 5 | NSC |
| 6 | OTHER FEDERAL AGENCY |
| 7 | ALLIED VETERAN |
| 8 | HUMANITARIAN EMERGENCY |
| 9 | SHARING AGREEMENT |
| 10 | REIMBURSABLE INSURANCE |
| 12 | CHAMPVA |
| 13 | COLLATERAL OF VET. |
| 14 | EMPLOYEE |
| 15 | HOUSEBOUND |
| 16 | MEXICAN BORDER WAR |
| 17 | WORLD WAR I |
| 18 | PRISONER OF WAR |

Table VA05 — Disability Retirement From Military

Disability Ret. From Military? (#.362) field of Patient (#2) file

| Value | Description |
| --- | --- |
| 0 | NO |
| 1 | YES, RECEIVING MILITARY RETIREMENT |
| 2 | YES, RECEIVING MILITARY RETIREMENT IN LIEU OF VA COMPENSATION |
| 3 | UNKNOWN |

Table VA06 — Eligibility Status

Eligibility Status (#.3611) field of Patient (#2) file

| Value | Description |
| --- | --- |
| P | PENDING VERIFICATION |
| R | PENDING RE-VERIFICATION |
| V | VERIFIED |

Table VA07 — Race

Abbreviation (#2) field of Race (#10) file

| Value | Description |
| --- | --- |
| 1 | HISPANIC, WHITE |
| 2 | HISPANIC, BLACK |
| 3 | AMERICAN INDIAN OR ALASKA NATIVE |
| 4 | BLACK, NOT OF HISPANIC ORIGIN |
| 5 | ASIAN OR PACIFIC ISLANDER |
| 6 | WHITE, NOT OF HISPANIC ORIGIN |
| 7 | UNKNOWN |

| TableVA08 — Religion (user defined) |
| --- |
| This table contains VA Religion codes. |
| Code (#3) field of Religion (#13) file. |
| Value | Description |
| 0 | CATHOLIC |
| 1 | JEWISH |
| 2 | EASTERN ORTHODOX |
| 3 | BAPTIST |
| 4 | METHODIST |
| 5 | LUTHERAN |
| 6 | PRESBYTERIAN |
| 7 | UNITED CHURCH OF CHRIST |
| 8 | EPISCOPALIAN |
| 9 | ADVENTIST |
| 10 | ASSEMBLY OF GOD |
| 11 | BRETHREN |
| 12 | CHRISTIAN SCIENTIST |
| 13 | CHURCH OF CHRIST |
| 14 | CHURCH OF GOD |
| 15 | DISCIPLES OF CHRIST |
| 16 | EVANGELICAL COVENANT |
| 17 | FRIENDS |
| 18 | JEHOVAH'S WITNESS |
| 19 | LATTER-DAY SAINTS |
| 20 | ISLAM |
| 21 | NAZARENE |
| 22 | OTHER |
| 23 | PENTECOSTAL |
| 24 | PROTESTANT, OTHER |
| 25 | PROTESTANT, NO DENOMINATION |
| 26 | REFORMED |
| 27 | SALVATION ARMY |
| 28 | UNITARIAN; UNIVERSALIST |
| 29 | UNKNOWN/NO PREFERENCE |
| 30 | NATIVE AMERICAN |
| 31 | BUDDHIST |

| Table VA11 — Period of Service |
| --- |
| Value | Description |
| 0 | KOREAN |
| 1 | WORLD WAR I |
| 2 | WORLD WAR II |
| 3 | SPANISH AMERICAN |
| 4 | PRE-KOREAN |
| 5 | POST-KOREAN |
| 6 | OPERATION DESERT SHIELD |
| 7 | VIETNAM ERA |
| 8 | POST-VIETNAM |
| 9 | OTHER OR NONE |
| A | ARMY--ACTIVE DUTY |
| B | NAVY, MARINE—ACTIVE DUTY |
| C | AIR FORCE—ACTIVE DUTY |
| D | COAST GUARD—ACTIVE DUTY |
| E | RETIRED, UNIFORMED FORCES |
| F | MEDICAL REMEDIAL ENLIST |
| G | MERCHANT SEAMEN—USPHS |
| H | OTHER USPHS BENEFICIARIES |
| I | OBSERVATION/EXAMINATION |
| J | OFFICE OF WORKERS COMP |
| K | JOB CORPS/PEACE CORPS |
| L | RAILROAD RETIREMENT |
| M | BENEFICIARIES-FOREIGN GOV |
| N | HUMANITARIAN (NON-VET) |
| O | CHAMPUS RESTORE |
| P | OTHER REIMBURS. (NON-VET) |
| Q | OTHER FEDERAL - DEPENDENT |
| R | DONORS (NON-VET) |
| S | SPECIAL STUDIES (NON-VET) |
| T | OTHER NON-VETERANS |
| U | CHAMPVA—SPOUSE, CHILD |
| V | CHAMPUS |
| W | CZECHOSLOVAKIA/POLAND SVC |
| X | PERSIAN GULF WAR |
| Y | CAV/NPS |
| Z | MERCHANT MARINE |

Table VA12 — Type of Insurance

| Value | Description |
| --- | --- |
| 0 | NO INSURANCE |
| 1 | MAJOR MEDICAL |
| 2 | DENTAL |
| 3 | HMO |
| 4 | PPO |
| 5 | MEDICARE |
| 6 | MEDICAID |
| 7 | CHAMPUS |
| 8 | WORKMANS COMP |
| 9 | INDEMNITY |
| 10 | PRESCRIPTION |
| 11 | MEDICARE SUPPLEMENTAL |
| 12 | ALL OTHER |

Table VA13 — VTQ Query Name

| Name | Function |
| --- | --- |
| VTQ_PID_ICN_LOAD_1 | Used to tell MPI that site is in initialization phase |
| VTQ_PID_ICN | Used to inquire to the MPI without any addition to MPI |

| Table VA14 — VTQ Selection Criteria |
| --- |
| Field | HL7 Field Number |
| Social Security Number | 00122 |
| Date of Birth | 00110 |
| Patient Name | 00108.1 (sub field Last Name field number) |
| Optional fields included: (can be used to refine close matches) |
| First Name | 00108.2 |
| Middle initial or name | 00108.3 |
| Name Suffix | 00108.4 |
| Name Prefix | 00108.5 |
| Birth Place City | 00126.1 |
| Birth Place State | 00126.2 (City and State are defined as separate fields in the MPI and are separated here using the decimal sub-numbers 126.1 and 126.2.) |
| Mothers maiden (last) name | 00109.1 |
| Sex | 00111 |
| Date of death | 00740 |
| Patient primary Facility | 00756 |
| ICN | 00105 |
| Servicing Facility | 00169 |

Table VA15 — Employment Status

| Value | Description |
| --- | --- |
| 1 | EMPLOYED FULL TIME |
| 2 | EMPLOYED PART TIME |
| 3 | NOT EMPLOYED |
| 4 | SELF EMPLOYED |
| 5 | RETIRED |
| 6 | ACTIVE MILITARY DUTY |
| 7 | UNKNOWN |

# Footnotes

According to the HL7 Standard, the maximum length of this element is 2.

According to the HL7 Standard, the maximum length of this element is 20.

This element is also found in the Patient Identification (PID) segment.

This element is also found in the Patient Identification (PID) segment.

The length of the observation value field is variable, depending upon value type. See OBX-2-value type.

May repeat for multipart, single answer results with appropriate data types, e.g., CE, TX, and FT data types.